## Slide 1: NAECA III Product Training
March 2015

## Slide 2: NAECA III Requirements
Gallons | Current | April 16, 2015
 | Electric | Electric
30 | 0.93 | 0.95
40 | 0.92 | 0.95
50 | 0.90 | 0.95
55 | 0.90 | 0.94
66 | 0.88 | 1.98
80 | 0.86 | 1.97
120 | 0.81 | 1.92
HPWH
A. O. Smith Confidential – Internal Use Only
Volume based calculation with new criteria for larger capacity models > 55 gallons
  Increase for ≤ 55 gal capacities a challenge for units already very efficient
  Increase for > 55 gal levels substantial, requiring technology change to heat pump water heaters

## Slide 3: Electric Objective & Scope
Develop electric portfolio to meet NAECA III minimum efficiency regulatory requirements including:
  Standard electric
  Mobile Home
Offer flexible options where feasible
Provide technology upsell
Leverage premium Energy Star qualified heat pump product
  Already compliant w/ Energy Star 3.0
Standardize features & design

## Slide 4: NAECA III Exemptions
Table Top only standard electric model granted exemption because of unique form factor
  We are standardizing product design
Compact/Utility <20g not subject to DOE reporting
Solar & storage tanks exempt
Standard 65/66, 80 & 119 gallon models discontinued

## Slide 5: Electric Overview
New models 28 through 55 gallons
  Achieve EF with increased foam, addition of external insulating blanket
  Provide flexibility in models where footprint is issue; lowboy, 50T, 30S
>55 gallon heat pump technology
  Broad portfolio w/ 50, 66, & two styles 80 gallon (short or tall)
  Energy Star qualified, high First Hour Rating, low sound level

## Slide 6: Product Standardization
Electric Standardization changes concurrent with new NAECA III portfolio
  Junction box
  Nipples installed
  Thermostat
Overall (Gas & Electric) feature standardization
  Combination dip tube nipple assembly
  Ported ball type drain valve
  Warranty terms 6/6, 10/6, 10/10
  Window Gray paint for jacket/trim

## Slide 7: Electric Element Changes
Standard 6/6 & 10/6
  Copper upper 4500W element
  Incoloy lower 4500W element; resist scale
Premium 10/10
  Dual Incoloy 5500W elements; resist scale, faster recovery
  Electronic thermostat replaces electromechanical

## Slide 8
Junction box design changes from round/painted to rectangular/galvanized
  Internal ground screw
  ½” & ¾” conduit ready
Standardization - Junction Box

## Slide 9: Standardization - Thermostat
APCOM thermostat now standard production on all residential electric
New thermostat bracket
TOD available for service replacements

## Slide 10: External Insulating Blanket
Ships loose in carton corner
Designed for easy field installation
  Vinyl backing
  Safety labels
  Cutouts for data plate & junction box
  For top or side connect
  Kit includes instructions & tape
Thickness is 3” fully expanded (optimal insulating capability), may be compressed to ¾” for clearance
Spec sheet dimensions of blanket models listed WITHOUT the blanket

## Slide 11: 6/6 & 10/6 Tall Electric Models
* Denotes model with additional external 3” fiberglass insulation blanket. Dimensions shown do not include the blanket.

## Slide 12: 6/6 & 10/6 Short Electric Models
Gallon Capacity | Current Model | Current Height (Inches) | Current Diameter (Inches) | NAECA-III Model | Height (Inches) | Diameter (Inches)
30 | 30 Short/Reg | 36-1/2 | 20-1/2 | 30 Short/Reg | 39-3/4 | 22
30 |  |  |  | 30 Short/Reg Blkt * | 39 | 20
40 | 40 Short/Reg | 44 | 20-1/2 | 40 Short/Reg | 50 | 22
50 | 50 Short/Reg | 48 | 22 | 50 Short/Reg | 49-3/4 | 24
* Denotes model with additional external 3” fiberglass insulation blanket. Dimensions shown do not include the blanket.

## Slide 13: 6/6 & 10/6 Lowboy Electric Models
LOWBOY TOP CONNECT |  |  |  |  |  |  | 
Gallon Capacity | Current Model | Current Height (Inches) | Current Diameter (Inches) | NAECA-III Model | Gallon Capacity | Height (Inches) | Diameter (Inches)
30 | 30 Low | 30 | 22 | 30 Low | 28 | 31-1/4 | 24
30 | 30 Low Blkt* | 30 | 20 | 30 Low Blkt* | 28 | 30 | 22
38 | 40 Low | 31-1/4 | 23 | 40 Low | 38 | 31-3/4 | 26
38 | 40 Low Blkt* | 32-1/4 | 24 | 40 Low Blkt* | 38 | 31-3/4 | 24
50 | 50 Low | 34 | 26-1/2 | Discontinued |  |  | 
LOWBOY SIDE CONNECT |  |  |  |  |  |  | 
Gallon Capacity | Current Model | Current Height (Inches) | Current Diameter (Inches) | NAECA-III Model | Gallon Capacity | Height (Inches) | Diameter (Inches)
30 | 30 Low | 30 | 22 | 30 Low | 28 | 31-1/4 | 24
30 |  |  |  | 30 Low Blkt* | 28 | 30 | 22
38 | 40 Low | 30-1/2 | 23 | 40 Low | 38 | 31-3/4 | 26
38 |  |  |  | 40 Low Blkt* | 38 | 31-3/4 | 24
* Denotes model with additional external 3” fiberglass insulation blanket. Dimensions shown do not include the blanket.

## Slide 14: Mobile Home Electric
MODEL | Hgt | Dia
30L | 28 3/4 | 22
30T | 45 | 18
40S/R | 47 1/4 | 20
MODEL | Hgt | Dia
30L * | 30 | 22
30T | 46 3/4 | 19
40S/R | 50 | 22
Today
2015
Side inlet/outlet
Enhanced flow brass drain
Available 240V/3500W or 120V/3000W, copper elements
6 year warranty
* Denotes model with additional external 3” fiberglass insulation blanket. Dimensions shown do not include the blanket.

## Slide 15: Electric Replacement Options Example
Original 50 Tall
54”
Tall
20”
Dia
New 50 Tall
60.5”
Tall
22”
Dia
Option 1
New 50 Tall Blkt*
60.25”
Tall
21”
Dia*
Option 2
New 40 Tall
60 1/2”
Tall
20”
Dia
Option 3
3” Foam insulation
2.5” Foam insulation
+ *External Blanket
40 Gallon Tank
+ Mixing Valve
Field installed
1.75” Foam insulation

## Slide 16: Mixing Valve Application
Works on electric & gas product
Option for multi-dwelling & applications where water heater shares space w/ HVAC air handler
Add on to heater installation
  Doesn’t improve EF, but can increase 1st hour performance
  Cons - added installation cost & complexity
  Pros - more hot water from smaller tank, avoid modifying the space

## Slide 17: New 66 & 80 Gallon Heat Pump
Low operating cost ~$194
High Energy Factor ~2.72
Superior hot water availability meets UPC
  66g = 81 gallon
  80g = 91 gallon
Quiet operation (51dBa, as w/50 gal)
Meets Energy Star 3.0 now
66g
80g “short”

## Slide 18: Heat Pump Electric
Today Std. Electric
2015 Heat Pump
Gallon Capacity | Current Model | Current Height (Inches) | Current Diameter (Inches) | NAECA-III Model | Height (Inches) | Diameter (Inches)
50 | 50 Tall | 54 | 20 | 50g HPWH | 63 | 22
66 | 66 Tall | 60 1/4 | 20 1/2 | 66g HPWH | 61 | 27
80 | 80 Tall | 60 1/2 | 22 1/2 | 80g HPWH | 69 | 27
120 | 120 Tall | 64 1/4 | 28 | No model available |  | 

## Slide 19: Heat Pump Replacement Options Example
Original 80 Tall
60.5”
Tall
22.5”
Dia
Option 1
Option 2
New 55 Tall
60”
Tall
24”
Dia
Option 3
Heat Pump
Requires
700 FT3
Open Space
Extra Field
Piping
55 Gallon Tank
+ Mixing Valve
option
1.75” Foam insulation
New 80g HPWH
68.5”
Tall
26.75”
Dia
Dual 40 Tall
60.33”
Tall
42”
Wide

## Slide 20: Electronic Models Overview
20

## Slide 21: Premium Electric Product Line
Available in 40 & 50 Tall, Short and 55 Tall
  Dual Incoloy 5.5KW 240V Elements
  10/10/1 warranty
Electronic Thermostat
  Grid Management ready
  Self Diagnostics
  Future remote ready

## Slide 22: Electronic Thermostat
More precise temperature sensing
  Thermistors more accurate & reliable than conventional thermostats
Dry-fire protection ensures trouble free installation
Diagnostics monitor operational parameters
  Ensure reliable operation & hot water availability
  Reported on ET via flashing LED (ESM is primary)
No single point of failure – operates with a failed element
  Provides connectivity for Smart Grid & home automation connectivity

## Slide 23: Electronic Thermostat User Interface
Operating Modes; Normal, Saver, Vacation
  Energy Saver Algorithm automatically adjusts to consumer hot water use, reducing standby heat loss up to 25%
  Vacation mode sets temperature 60° to conserve electricity
User-Friendly Interface integrated in upper element cover
  Heads-up digital display
  Back-lit buttons for easy operation
    Temperature, mode selection in user interface
  Icons notify consumer - element on, error code (Alert), unit is under Smart Grid management, or keypad is locked
  Access lock feature keeps children from resetting
Diagnostic reporting in LDC
  Monitors 1) dry-fire detection, 2) ET failure, 3) lower thermistor failure, 4) upper element failure, 5) lower element failure, 6) ESM defective
mode selection buttons
temperature & lock selection buttons

## Slide 24: AO Smith SmartPort
SmartPort is a communications port:
  Facilitates water heater connectivity to home automation, remote thermostat, utility demand response, & similar connectivity applications
  Mounted on top of premium electric models, and on the front of new heat pump models

## Slide 25: Smart Grid CEA-2045 Bridge Module
Bridge module plugs into SmartPort
Communications module links water heater to utility demand response application(s)
Bridge module features
  LED status indicator
  Reset button
  Audible alarm 85dB
  Accessory port
Accessory port options
  Leak detection module provides remote notification of leak

## Slide 26: WiFi Controller Capable
Proprietary control module for future home automation application
  WiFi connectivity allows remote operation & status monitoring
  Plugs into the SmartPort
Plug & play link to homeowner’s internet router
  Cloud based application to Smart Phone, Tablet, Pad, or Computer
Features
  LED status indicator
  Reset button
  Audible alarm 85dB
  Accessory port
Options
  Leak detection module for accessory port will provide remote notification of leak condition